## Slide 2
Modelling synchrotron radiation beamlines with
OASYS
Transport of photons in a Beamline
Manuel Sanchez del Rio
srio@esrf.fr
Advanced Analysis & Precision Unit, MEG/ISDD, ESRF
March 22nd 2024
ShadowOui

## Slide 3: Transport of photons in a Beamline
Outline:
Introduction to ray tracing
Simulation of a beamline:
  Mirror focusing (KB): size at sample
    Effect of aberrations
    Source dimensions
  Double-crystal monochromator
    Energy resolution
    Crystal coupling: (+,-) (+,+)
  Full beamline: Flux and power that arrive to the sample
ShadowOui

## Slide 4: RAY TRACING (SCHEMATIC)
p
y
z
x
q
z
x
x
y
z
Energy, Intensity

## Slide 5: REFERENCES AND Continuation planes
Source Plane for O.E.1
O.E.1
O.E.2
Image Plane for O.E.1
Source Plane for O.E.2
Optical axis
Note that (VERY IMPORTANT!):
The y (column 2) coordinate is along the beam direction
The position (Source Plane Distance), orientation (O.E. Orientation Angle) of any o.e. is always referred to the previous one
Source Plane and Image Plane for each optical element are the “Continuation Planes”
The frame is rotated if one o.e. is rotated

## Slide 6: The beamline
Optical components that could be present in a beamline:
Source
U42 @ 5keV
Front end
Primary slits
Primary mirrors
Plane Ni 7 mrad
Monochromator
Double crystal
Si 111
Focusing system
Sample
KB mirrors
27.2 m
51.5 m
51.59 m
51.65 m
KB slits
51 m

## Slide 7: Mirror focusing Kirkpatrick-Baez (MODEL 1)

## Slide 8: Monochromator (MODEL 2)
Si 111 (+,-) @ 5keV Si 111 (+,+) @ 5keV Si 333 (+,-) @ 15keV Si 333 (+,-) @ 15keV
0.58 eV
0.54 eV
0.38 eV
0.1 eV
(+,-)
(+,+)

## Slide 9: Full beamline (MODEL 3)
SIZE RESOLUTION FLUX
0.6 eV
---> Integrated Flux : 1.25321e+13 ph/s

## Slide 10: Comparison with XOPPY [consistency] (MODEL 4)
Optical components that could be present in a beamline:
1.32 x 1013 photons/s
5 KeV
Source
U42 @ 5keV
Primary slits
Primary mirrors
Plane Ni 7 mrad
Monochromator
Double crystal
Si 111
Focusing system
Sample
KB mirrors
51 m
KB slits
1 x 1 mm2

## Slide 11: RESOURCES
You have more material here:
the ShadowOuiTutorial: https://github.com/oasys-kit/ShadowOui-Tutorial
The OASYS Schools: https://github.com/oasys-kit/oasys_school
We did not treat important issues like:
Surface errors in mirrors [see tutorial example 20]
Focusing with lenses [CRLs, transfocators] [see tutorial example 24]
Hybrid ray tracing [to include coherence effects]
Wave optics calculations using the SRW code

## Slide 12
Additional Slides

## Slide 13: Approximating emission at resonance by Gaussians Onuki & Elleaume Undulators, Wigglers and their applications, CRC press, 2002
Undulator radiation approximated by Gaussians (at resonances) are not Fourier pairs (like beams following the Gaussian Shell-model)