## Slide 2
Modelling synchrotron radiation beamlines with
OASYS
Introduction
Juan Reyes Herrera
juan.reyes-herrera@esrf.fr
Advanced Analysis & Precision Unit, MEG/ISDD, ESRF
March 15th & 17th 2022

## Slide 3: Introduction to OASYS
Outline:
What is OASYS? What is its structure?
What kind of simulations can be performed with it
    Expected outcome of this OASYS tutorial

## Slide 4: What is OASYS?
OASYS (Orange Synchrotron Suite) is graphical environment for modelling synchrotron beamlines.
In OASYS, we can perform visual programing: using “boxes and arrows” to recreate a photon beamline
OASYS integrates different simulation strategies via the implementation of adequate simulation tools for X-ray Optics
https://www.aps.anl.gov/Science/Scientific-Software/OASYS

## Slide 5: Modelling a beamline
A synchrotron beamline is the instrumentation that transports the synchrotron radiation to the sample (experimental end station)
Electron beam
Photon beam
Beamline
Optics hutch
Experimental hutch
Control hutch*
Insertion device
Hutch or cabin*

## Slide 6: Modelling a beamline with OASYS
Source
Bending magnet, wiggler or undulator
Optics
Experimental station
Slits, mirrors, crystals, filters, refractive lens, Fresnel lens, multilayers, etc.
Sample, detectors, etc.
Main components of the beamline:

## Slide 7: Modelling a beamline with OASYS
Sources:
Optics:
Allowing to get at the
Sample:
Energy distribution, intensity (photon flux), beam size and divergence, etc.
The visual programing boxes, in OASYS, are called Widgets and they represent optical components, including a wide variability of tools, example:

## Slide 8: Modelling a beamline with OASYS
The Widgets are connected as a workflow (or dataflow) in the OASYS canvas:
Canvas
Widgets
Connectors
Toolbox
OASYS Workflow

## Slide 9: Full beamline model
ESRF-ID21
Higher Harmonic Rejection Mirrors
Double Crystal
Monochromator
KB Mirrors system

## Slide 10: Introduction to OASYS
Computer simulation of light sources and optical components is a mandatory step in the design and optimization of synchrotron and FEL radiation beamlines
different codes for numerical simulations are available, implementing different physical approaches
RAY-TRACING
WAVEFRONT
PROPAGATION
Shadow
RAY
XRT
McXtrace
SRW
PHASE
WISE
WOFRY
COMSYL
Incoherent X-ray beams Fully coherent X-ray beams

## Slide 11: ORANGE
Orange is a component-based visual programming software package for data visualization, machine learning, data mining, and data analysis. [1].
[1] Demšar, J., Curk, T., and Erjavec, A. "Orange: Data Mining Toolbox in Python," Journal of Machine Learning Research 14, 2349−2353 (2013). https://orange.biolab.si

## Slide 12: OrAnge SYnchrotron Suite
SRW
XOPPY
Orange
SYNED
COMSYL
Utilities
WOFRY
SHADOWOUI
Luca Rebuffi (ANL) & Manuel Sánchez del Río (ESRF)
L. Rebuffi, M. Sanchez del Rio, "OASYS (OrAnge SYnchrotron Suite): an open-source graphical environment for x-ray virtual experiments”, Proc. SPIE 10388, 103880S (2017)​​​​​. DOI: 10.1117/12.2274263.

## Slide 13: OASYS interoperability
XOPPY
SRW
SHADOW
SYNED
DABAM

## Slide 14: Other OASYS features
Open Source, many synchrotron facilities are developing their own customized widgets, Add-ons, for example:
https://github.com/oasys-als-kit
https://github.com/oasys-lnls-kit
https://github.com/oasys-elettra-kit
https://github.com/oasys-esrf-kit *
* Add-ons installation example

## Slide 15: Other OASYS features
Python has been chosen as the main programming language, and code can be included in the workflow

## Slide 16: Outcome from this tutorial
Calculate main characteristics of synchrotron source (Bending magnets and Insertion devices).
Calculate the heat-load on different beamline components.
Simulating beamline optics by ray-tracing to obtain main parameters of the beam, e. g., size and divergence, energy resolution, intensity/flux.
Understand basic principles of X-ray optics: Mirrors and Crystals.
Basic concepts about coherence