## Slide 1: HERCULES 2021 - TUTORIAL Modelling SR beamlines using OASYS
Manuel Sánchez del Río
AAMP, MEG, ISDD, ESRF
2021 March 3rd 14:00

## Slide 2: Outline
Introduction to OASYS
XOPPY toolbox: Source emission and characteristics of optical elements. Power transport
ShadowOUI: Ray tracing SR beamlines
  Mirror aberrations
  Crystal systems
  Lenses
WOFRY and SRW: coherent beam transport:
  Simple examples with WOFRY
  Introduction to Partial coherence

## Slide 3: Outcome Calculate main characteristics of synchrotron sources (dipoles and IDs) Simulating beamline optics by ray-tracing to obtain main parameters of beam size, energy resolution and flux Understand basic principles of x-ray optics: Reflective (aberrations, slope errors), Diffractive (dispersion) and Refractive (chromatic aberrations) A few concepts about coherence

## Slide 4: Outline
Introduction to OASYS
XOPPY toolbox: Source emission and characteristics of optical elements. Power transport
ShadowOUI: Ray tracing SR beamlines
  Mirror aberrations
  Crystal systems
  Lenses
WOFRY and SRW: coherent beam transport:
  Simple examples with WOFRY
  Introduction to Partial coherence

## Slide 5: The OASYS Project
OASYS = OrAnge SYnchrotron Suite
A common platform to build synchrotron-oriented User Interfaces that communicate
The upper layer of the application presented to the user
Open Source & Python technology
Luca Rebuffi
Manuel Sanchez del Rio
Luca Rebuffi, Manuel Sanchez del Rio (2017)
OASYS (OrAnge SYnchrotron Suite) : an open-source graphical environment for x-ray virtual experiments
Proc.SPIE 10388: 10388-10388. http://dx.doi.org/10.1117/12.2274263
https://oasys-kit.github.io/
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 6: Synchrotron Virtual Experiments
Storage Ring
(e- optics)
Radiation devices
(e- -> g)
Beamline
(g optics)
Sample
(g -matter interactions)
Beamline Experiment Chain
ShadowOui
WOFRY
XOPPY
X-ray server
WISE
COMSYL
Suite of Add-ons
SRW
Upper layer based
on ORANGE (U Ljubljana)

## Slide 7: The OASYS language

## Slide 8: Multiple tools in the same environment

## Slide 9: References
Official Web Page
OASYS Publications
https://www.aps.anl.gov/Science/Scientific-Software/OASYS
or https://oasys-kit.github.io/
M. Sanchez del Rio, L. Rebuffi, J. Demšar, N.Canestrari and O. Chubar, A proposal for an open source graphical environment for simulating X-ray optics, Proc. SPIE 9209, 92090X (2014)​
M. Sanchez del Rio, D. Bianchi, D. Cocco, M. Glass, M. Idir, J. Metz, L. Raimondi, L. Rebuffi, R. Reininger, X. Shi, F. Siewert, S. Spielmann-Jaeggi, P. Takacs, M. Tomasset, T. Tonnessen, A. Vivo and V. Yashchuk, DABAM: an open-source database of X-ray mirrors metrology, J. Synchrotron Rad. 23 (2016).
L. Rebuffi, M. Sanchez del Rio, ShadowOui: A new visual environment for X-ray optics and synchrotron beamline simulations, J. Synchrotron Rad. 23 (2016)
L. Rebuffi, M. Sanchez del Rio, Interoperability and complementarity of simulation tools for beamline design in the OASYS environment, Proc. SPIE 10388, 1038808 (2017)​.​​​​​​
L. Rebuffi, M. Sanchez del Rio, OASYS (OrAnge SYnchrotron Suite): an open-source graphical environment for x-ray virtual xperiments, Proc. SPIE 10388, 103880S (2017)​​​​​.
X. Shi, R. Reininger, M. Sanchez del Rio, L. Assoufid, A hybrid method for X-ray optics simulation: combining geometric ray-tracing and wavefront propagation, J. Synchrotron Rad. 21, 669 (2014)
X. Shi, R. Reininger, M. Sanchez del Rio, J. Qian, L. Assoufid, X-ray optics simulation and beamline design using a hybrid method: diffraction-limited focusing mirrors, Proc. SPIE, 9209, 920909 (2014)

## Slide 10: Three sessions
XOPPY (tools) hercules_xoppy.ows
ShadowOUI (ray tracing) hercules_shadowoui.ows
WOFRY (wave optics) hercules_wofry.ows

## Slide 11
Computer simulation of light sources and optical components is a mandatory step in the design and optimization of synchrotron and FEL radiation beamlines
different codes for numerical simulations are available, implementing different physical approaches
RAY-TRACING
WAVEFRONT
PROPAGATION
Shadow
RAY
XRT
McXtrace
SRW
PHASE
WISE
WOFRY
COMSYL
Incorerent X-ray beams Fully coherent X-ray beams
X-ray optics for synchrotron and XFEL beamlines
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 12: From theory to software
Propagation of one wavefront.
One wavefront is coherent by nature.
A wavefront is approximated by a ray. Many rays are summed up to form a beam, that is incoherent.

## Slide 13: At HIGH ENERGIES, WE ARE FAR FROM DIFFRACTION-LIMIT (=FULLY COHERENCE) THEREFORE, ANY BEAMLINE SIMULATION MUST START WITH RAY TRACING (INCOHERENT BEAMS)
3.13 %
0.18 %
Source: ESRF Orange book
COMSYL calculation
U17 2m @ 17 keV (K=0.4842) L=2m

## Slide 14: Typical coherence beamline
How much
Coherent ?
Incoherent
Partial coherence optics

## Slide 15: Hierarchical approach to study beamline optics
Hand calculations (sizes divergences and distances define magnification, optical element reflectivities)
Ray tracing (starting from point sources, monochromatic beams, ideal optics, etc. then integrate finite sizes, polychromaticity, real optics with surface errors)
If coherence is important, apply wave optics
  Hybrid method: corrections to ray tracing
  1D prototyping (fast)
  2D full simulation
  Partial coherence (multielectron, coherent mode decomposition)

## Slide 16: Outline
Introduction to OASYS
XOPPY toolbox: Source emission and characteristics of optical elements. Power transport
ShadowOUI: Ray tracing SR beamlines
  Mirror aberrations
  Crystal systems
  Lenses
WOFRY and SRW: coherent beam transport:
  Simple examples with WOFRY
  Introduction to Partial coherence

## Slide 17: Source emission (XOPPY)
Undulator spectrum (flux or power versus E)
Undulator power density (power versus X,Y)
Undulator Spectrum (flux/power vs X,Y,E)
Undulator tuning curves
Wiggler spectrum Spectrum (flux/power vs X,Y,E)
BM Spectrum (flux/power vs E, angle)
Others

## Slide 18: Optical elements (XOPPY)
Attenuators
Mirrors
Multilayers
Crystals

## Slide 19
Undulator Memorandum
19
Undulator emission, after classical electrodynamics (e.g., Jackson, etc)
On resonance
mec2 = 0.51 MeV
On resonance approximation
Onuki & Elleaume Undulators, Wigglers and their applications, CRC press, 2002
Slit (2.1 x 1 mm2)
Slit (10 x 10 mm2)
~

## Slide 20: Courtesy: Boaz Nash
(FOR UNDULATORS, THESE FORMULAS ARE VALID AT THE WAIST, AT THE UNDULATOR RESONANCE, AND SUPOSSING GAUSSIAN EMISSION OF PHOTONS)
ShadowOui performs “numeric convolution” by Monte Carlo sampling of the electron beam [Gaussian] and photon emission [non Gaussian]

## Slide 21
Undulators: Power and spectral calculations
21
Maximum power is obtained at highest K (or B) corresponding to the minimum photon energy
The spectral range covered by undulator is shown by the Tuning Curves.

## Slide 22
22
Tips:
Calculate on aperture large enough to accept all the radiation
Select “modify slit” to calculate power on smaller slit and to calculate power density on mirror surface
6 sigma 1.32 mm
Mask
2x2 mm @ 25.4,=m
Or
2.1x2.1 @ 28m
Mirror:
400mm
2.1mm (mask)
Power density (Power vs X and Y)

## Slide 23
Flux and Spectral Power
23
Open Slit (10 x 10 mm2)
Slit (2.1 x 1 mm2)

## Slide 24
Spectral response of mirrors and attenuators (filters)
24
Second OASYS School – ANL APS - December 11-13, 2019
Interaction of radiation with matter
XOPPY
0.4 mm
Al
X-ray beam
X-ray beam
Mirror Angle
Ni coating

## Slide 25
Combined (X,Y,E) effect of optical elements

## Slide 26
Crystals: Zachariasen treatment for plane crystals
26
BRAGG or reflection
LAUE or transmission

## Slide 27
Crystals: Rocking curves
27
The rocking curve is the CONVOLUTION of the two diffraction profiles.
For a full discussion about rocking curves see: Masiello et al. J. Appl. Crystall. 47, 1304-1314 (2014)
FWHMR = 1 FWHM1
FWHMR = 1.4 FWHM1
FWHMR ~ 1.5 FWHM1
Si111 8 keV
=
=
=

## Slide 28
Mirror reflectivity F1F2
28

## Slide 29
Multilayer reflectivity
29

## Slide 30: Outline
Introduction to OASYS
XOPPY toolbox: Source emission and characteristics of optical elements. Power transport
ShadowOUI: Ray tracing SR beamlines
  Mirror aberrations
  Crystal systems
  Lenses
WOFRY and SRW: coherent beam transport:
  Simple examples with WOFRY
  Introduction to Partial coherence

## Slide 31
Trace (the beamline)
p
y
z
x
q
z
x
x
y
z
Energy, Intensity

## Slide 32
Continuation planes
Side View
Top View
Source Plane for O.E.1
Image Plane for O.E.2
O.E.1
O.E.2
Image Plane for O.E.1
Source Plane for O.E.2
Optical axis

## Slide 33
Note that (VERY IMPORTANT!):
The y(2) coordinate is along the beam direction
The position (Source Plane Distance), orientation (O.E. Orientation Angle) of any o.e. is always referred to the previous one
Source Plane and Image Plane for each optical element are the “Continuation Planes”
The frame is rotated if one o.e. is rotated

## Slide 34
SHADOW ray’s variables (columns)
Stored:
Computed:
**
* X’,Y’,Z’ is the direction vector (unitary), for small angles (always in SR) Y’<~1, and X’ and Z’ can be considered “divergences”
** Column 11 is energy in eV. Internally SHADOW stores the wavenumber 2 p / l in cm-1
*

## Slide 35: Optical elements
For each optics element SHADOW includes:
Geometrical model: how the direction of the rays are changed (reflected, refracted or diffracted)
Physical model: how the ray intensity (in fact electric fields) decreases because of the interaction
Structures along the surface =>playing with the direction
Structures in depth => playing with the reflectivity

## Slide 36: ShadowOUI Sources I

## Slide 37: Sources II (Wiggler and also mutiple BMs and Short IDs)

## Slide 38: Sources III (Undulator)
Fake Geometrical Source
(Gaussian spatial + Gaussian divergency)
789.938eV
806.060eV
814.121eV
Full Undulator
Single e-
Divergence:
Size:
Photon source:

## Slide 39: Optical Elements (mirrors) Geometrical model Physical model
Fresnel equations give the reflectivity as a function of angle and photon energy. As a consequence, one gets the critical angle:
Si s-reflectivity

## Slide 40: Optical Elements (gratings)
Geometrical model Physical model
No model (yet) in SHADOW for grating efficiency
SHADOW uses Fresnel equations like for mirrors
Figure from doi.org/10.5772/51044

## Slide 41: Optical Elements (crystals)
Geometrical model Physical model

## Slide 42: Mirrors and aberrations
q
p
R
r
Ellipsoid: Point to point focusing
Paraboloid: Collimating
Focalization in two planes
  Tangential or Meridional (ellipse or parabola)
  Sagittal (circle)
Demagnification: M=p/q
Easier manufacturing:
  2D: Ellipsoid => Toroid
  Only one plane: cylinder Ellipsoid (ellipse)=> cylinder (circle)
  Sagittal radius: non-linear (ellipsoid) => constant (cylinder) or linear (cone),
All mirrors produce aberrations

## Slide 43: Crystal monochromators
Theory of the Use of More Than Two Successive X-Ray Crystal Reflections to Obtain Increased Resolving Power J W. M. DuMond Phys. Rev. 52, 872 – (1937) http://dx.doi.org/10.1103/PhysRev.52.872
ex17_crystalmono.ows

## Slide 44: Crystal curvature and spectral resolution
Zero for Rowland mounting:
p = R sin(q) that for Bragg
symmetric reflection means
1:1 magnification

## Slide 45: X-ray Lenses
p
q

## Slide 46
CRL (COMPOUND REFRACTIVE LENSES) = replicate N lenses
Single interface
Lens
Compound Refractive Lens (CRL)
Transfocator
1996 Experimental demonstration of CRL
A. Snigirev et al Nature 384 (1996) 49
2011 Transfocator

## Slide 47: Outline
Introduction to OASYS
XOPPY toolbox: Source emission and characteristics of optical elements. Power transport
ShadowOUI: Ray tracing SR beamlines
  Mirror aberrations
  Crystal systems
  Lenses
WOFRY and SRW: coherent beam transport:
  Simple examples with WOFRY
  Introduction to Partial coherence

## Slide 48: Wave optics
Based on sampling a wavefront (monochromatoc and coherent), and propagate it (in free space and trough optical elements)
2D wavefront sampling is costly ~N^2
Propagation is expensive N^4 or N^2 if FFT
Optical elements modelled as thin objects
Parameter setting is complex

## Slide 49: Wavefront and Propagator discretization
Effect of the discretization: Replicas
Replicas can be avoided by increasing the sampling or by isolating the main feature at the image plane, if the replica are well separated.
Effect of under-sampling: Aliasing
Under-sampling produces an overlapping of the replicas, thus completely distorting the expected result. This effect is called aliasing.

## Slide 50: SRW (Oleg Chubar, BNL)
https://github.com/ochubar/SRW
Chubar, O. and Ellaume, P.: Accurate and efficient computation of synchrotron radiation in the near field region. Proceedings of the 6th European Particle Accelerator Conference - EPAC-98, pages 1177-1179
Chubar, O.: Wavefront calculations. Proc. SPIE, 4143:48-59 (2001)
Chubar, O., Berman, L., Chu, Y. S., Fluerasu, A., Hubert, S., Idir, M., Kaznatcheev, K., Shapiro, D. Shen, Q. and Baltser, J.: Development of partially-coherent wavefront propagation simulation methods for 3rd and 4th generation synchrotron radiation sources. Proc. SPIE, 8141:814107 (2011)
Chubar, O.: Recent updates in the "Synchrotron Radiation Workshop" code, on-going developments, simulation activities, and plans for the future. Proc. SPIE, 9209:920907 (2014)
Chubar, O., Rakitin, M., Chen-Wiegart, Y.K., Chu, Y.S., Fluerasu, A., Hidas, D. and Wiegart, L.: Main functions, recent updates, and applications of Synchrotron Radiation Workshop code. Proc. SPIE, 10388:1038805 (2017)
Chubar, O. and Celestre, R.: Memory and CPU efficient computation of the Fresnel free-space propagator in Fourier optics simulation. Opt. Express 27, 28750-28759 (2019)
OASYS interface by Luca Rebuffi

## Slide 51: WOFRY (OASYS team)
Simpler use
Basic wavefronts (plane waves, spherical waves)
1D and 2D modes (less expensive)
Approximated undulator sources
Effective propagators
Not as complete as SRW but growing fast
Good for prototyping beamlines

## Slide 52: Propagators
1D
2D
Fresnel
Fresnel (convolution)
Integral
Fresnel Zoom
Fresnel Zoom Scaled

## Slide 53: Zoom Propagator
G. Pirro, Master Thesis (2017)
https://github.com/oasys-kit/documents/blob/master/zoom_propagator_pirro_thesis.pdf

## Slide 54
wofry_examples.ows simple propagation cases
Aperture=0.4 mm, E=17225 eV, D=5cm
F=D
F=D/2
F=D/2
Converging spherical +
Propagation (D)
Plane + Lens (F=D)+ Propagation (D)
Spherical divergent+ Lens (F=D/2)+ Propagation (D)
Gaussian+ Propagation(D)+ Lens (F=D/2)+ Propagation (D)
54

## Slide 55: 2D Oversimplified Beamline
The diffraction by a DxD square aperture of a collapsing spherical wavefront has an intensity distribution proportional to sinc2(kDx/2f ) sinc2(kDy/2f), where k=2π/λ, x(y) is the horizontal (vertical) coordinate, and f is the distance aperture-focus (D/f is the divergence). Considering that the FWHM of sinc2(x) is approximately 2.78, one obtains a FWHM=0.885 * wavelength / divergence=18nm
Theoretical consideration

## Slide 56: Partial coherence

## Slide 57
2D functions
4D function
W ~ 108 – 1012 (Gb-Tb)
Propagate: 4D integrals
Store m x N x N Propagate: 2D integrals
Partial coherence is due to the electron beam emittance
Multielectron Calculation (SRW)
Coherent mode decomposition
http://dx.doi.org/10.1209/0295-5075/119/34004 Mark Glass, Manuel Sanchez del Rio (2017) Coherent modes of X-ray beams emitted by undulators in new storage rings EPL (Europhysics Letters) 119

## Slide 58: COMSYL EBS SOURCE (CF 0.028)
https://youtu.be/h24RrJZaQ80

## Slide 59: Example approximating the Undulator by the Gaussian Shell-model

## Slide 60: SIMPLE CASE: 1D Gaussian SHELL-MODEL
Both intensity (Spectral Density) and correlation (Spectral Degree of Coherence) are Gaussians
sI>>sm the source is mostly incoherent (quasi homogeneous)
sI<<sm is mostly coherent
I
I
In 2D (H x V)
2D Hermite-Gaussian or
TEMnm modes
Eigenvalues
Eigenfunctions
(Hermite-Gaussian modes)
Magic property: Propagation invariance
In the first mode (Gaussian) :

## Slide 61: The spectrum of coherent modes
Coherent: b>>
incoherent
In general we cannot apply Gaussian Shell-model to synchrotron
b<<
Eigenvalues
Mode occupation:
Coherent fraction: